## Slide 1: High-level benchmarking Scientific Research Organisation – 150,000sq.m
Jo Harris

## Slide 2: Scope of project
High-level benchmark required
Initial view on delivery process and options

## Slide 3: Methodology
One day to visually inspect a representative sample
Information on:
  dimensions of the building
  breakdown of costs
  costs of specialist sub-contract works
Use IFPI’s EstatesMaster Facilities Benchmarking and Cost Prediction program at High-level (Level 1)
Initial consideration and commentary for maintenance delivery and management
Discuss preliminary findings
Written Report
Notes: of the buildings and building services to establish the complexity and scale of operations

## Slide 4: Information made available
Total floor area – 150,000 m2 GIA
Expenditure on reactive and planned maintenance – approx. £5m p.a.
Specialist sub-contracts information - Compressed Air only received
500 planned maintenance tasks recorded on the asset data-base
2800 reactive maintenance requests p.a.(estimated)
The M+E maintenance of the specialist laboratory buildings have an independent maintenance regime and are excluded

## Slide 5: Enhancements
Used Level 2 of EstatersMaster because of the apparent discrepancy between the results from Level 1 and the £5m budget
More site details reviewed
  Pump list – Heating and Cooling
  Schedule of Air Compressors
  Schedule of LPHW Boilers
  Schedule of Cranes and Lifting Equipment
  Schedule of Lifts
  Schedule of Fire Alarm Devices
  Fabric maintenance included

## Slide 6: Results
Omitting the experimental laboratories entirely; not skewed by the presence of a large area of minimally serviced building.
Benchmark range from £1.1 - £1.4 m p.a.
Median benchmark for maintenance of £1.25m p.a.
£17 per m² GIA (after removing the specialist buildings)
Intelligent Client Function not working with an adhoc approach to maintenance management and ‘fire-fighting’

## Slide 7: How to increase accuracy
Scope - work outside the scope of the cost centre
Answers - quality and difficulty of the services
Data - building details

## Slide 8: Adjustment for out-of scope items
Scope – Life-cycle replacement
      Minor building works

## Slide 9: How to increase accuracy
Scope - work outside the scope of the cost centre
Answers - quality and difficulty of the services
Data - building details

## Slide 10: Summary
High level benchmark to review current delivery
Level of information is the key to an accurate result
Notes: The more information you put in the better the result